## Slide 1
Dr. Wenyi Wang, Dr. Nader Sawalhi and Dr. David Blunt
Defence Science and Technology Group (DSTG)
Melbourne, Australia
(A HUMS2025 Presentation)
The HUMS2025 Data Challenge Dataset
The 14th DSTG International Conference on
Health & Usage Monitoring Systems (HUMS2025)
Melbourne, Australia

## Slide 2
Background – why we did the test (gear tooth surface fatigue/wear)
Unexpected damage – a cracked casing
Deriving a dataset for HUMS2025 Data Challenge
  Pinion/bevel hunting-tooth synchronous signal average (H-SSA)
  Selected raw data
Outline
Expected type of failure

## Slide 3
Background
Gear tooth surface fatigue or spalling is a common failure mode in helicopter and general industrial gearboxes.
There is a scarcity of good failure progression data related to gear tooth spalling faults or tooth degradation by contact fatigue.
DSTG established a test program to generate a set of Inductive Wear Debris Sensor (MetalSCAN) data, along with accelerometer vibration data.
Purpose: to monitor the progression of 3 x electric discharge machined (EDM) notches (seeded faults) from initial pitting to advanced stage spalling under controlled conditions.
Use real-time monitoring and analyses of the wear debris and vibration data to monitor progress and prevent catastrophic gearbox failure.

## Slide 4
22 days of overload testing
89 load cycles (100%-125%-150%-125% rated load)
Some increase in wear debris counts (~100 accumulated ferrous metal particles)
Not as many WD particles as expected
Particles – some gear material
Unexpected Damage – a Cracked Casing
Notes: Casing material = ZE41A Magnesium Alloy (1.84 g/cm^3, steel is 7.85 g/cm^3)

## Slide 5
Originated on or near the spline in the upper casing that holds the epicyclic ring gear likely before the test began
Fatigue crack propagated in two directions
  Horizontally towards a threaded hole for a stud securing the gearbox to a support strut
  Vertically up into the top of the upper casing
The fatigue crack ultimately resulted in an overload-induced fracture that caused a section of the casing to break away.
Note that the ring gear itself was still intact so that the planetary gear set was still held together.
Note: this casing crack has no bearing on the quality of the gearbox because the test gearbox was: (a) retired from service and no longer fit to fly; and (b) was subjected to severe overload (125% and 150% of the rated continuous load) for most of this test in order to accelerate the fault progression, and similar high loads in previous tests.
Upper Casing Fracture Surface
spline

## Slide 6
The HUMS2025 Data Challenge dataset contains vibration data from the last 86 load cycles (out of 89 cycles)
Each cycle has the loading sequence 100%-125%-150%-125% with 20 minutes at each load level
There are 1830 pinion/bevel hunting-tooth signal averages at the three load levels, i.e. 100%, 125% and 150% rated load (4 vibration channels)
Raw vibration data: 204 selected files at 100% rated load; 210 selected files at 125% rated load
Each raw data file has 30 seconds of data sampled at 65573.77049180328 Hz (~2^16=65536 Hz,)
  Four vibration channels,
  One tachometer channel at the same rate and length
Dataset for the HUMS2025 Data Challenge
Notes: Materials: casing = non-ferrous (ZE41A); spline = non-ferrous (ZE41A); ringGear = ferrous AISI-9310

## Slide 7
Real-time Monitoring

## Slide 8
Real-time Monitoring – Pinion-SSA Residual method

## Slide 9
Real-time Monitoring – SSA-Pinion by Unified Change Detection

## Slide 10
Real-time Monitoring – SSA-Pinion Unified Change Detection (GMH removed)
Day 12 & 15

## Slide 11
Questions ???

## Slide 12
We would like to acknowledge and thank the invaluable contribution and support provided through the different stages of the pinion gear test project from:
The team that designed and carried out the Bell-206B MRG pinion gear seeded fault test led to the generation of the casing crack dataset for the HUMS2025 Data Challenge, the DSTG test team members are: Andrew Becker, James Harris, Peter Stanhope, Riyazal Hussein, Jordan Carroll, Brad Bielenberg, Eric Lee and Anna Houston;
The crack fractography analysts (Vui-Tung Mau, James Niclis of QinetiQ and Cathy Smith, Nick Athiniotis of DSTG) for assessing and quantifying the casing fracture surface;
DSTG Platforms Division management for their continued support for HUMS Conference series.
Acknowledgement